How to control the multiple-comparison problem in SAM statistics

Zaifeng Gao HUJ

General procedure using SAM:

SAMcov → SAMwts → SAMerf→ adwarp → 3dttest
(http://kurage.nimh.nih.gov/meglab/Meg/Meg)

Problem: 3dttest conducts simple t-test voxel by voxel, it does not control the multiple-caparison problem.

Solved Solutions:
 AFNI provide two ways :
False Discovery Rate (RDR): expected proportion of false positive voxels among all detected voxels (the proportion of the none-significant voxels in the voxel showing to be significant)

        3dDeconvolve, 3dANOVAx, 3dttest, and 3dNLfim now compute FDR curves for all statistical sub-bricks and store them in output header. AFNI now shows p- and q-values below the threshold slider bar.

        Therefore, you can control the type-I error by using q, for instance, set q=0.05.

Disadvantage: FDR is conservative (q-values are too large) when voxels are positively correlated (e.g., from spatially smoothing).

Monte Carlo simulations with program 3dClustSim.
  (http://afni.nimh.nih.gov/pub/dist/doc/program_help/3dClustSim.html)

1. open terminal
2. run 3dClustSim with the related parameters:
  3dClustSim -fwhm 7 -pthr 0.0005 0.0004 0.0003 0.0002 0.0001 0.00001 -nodec
  ++ 3dClustSim: AFNI version=AFNI_2010_10_19_1028 (Nov 23 2010) [64-bit]
  ++ Authored by: RW Cox and BD Ward
  Simulating:0123456789.0123456789.0123456789.0123456789.0123456789.
  # 3dClustSim -fwhm 7 -pthr 0.0005 0.0004 0.0003 0.0002 0.0001 0.00001 -nodec
  # Grid: 64x64x32 3.50x3.50x3.50 mm^3 (131072 voxels)
  #
  # CLUSTER SIZE THRESHOLD(pthr,alpha) in Voxels
  # -NN 1 | alpha = Prob(Cluster >= given size)
  # pthr | 0.100 0.050 0.020 0.010
  # ------ | ------ ------ ------ ------
  0.000500 12 14 16 17
  0.000400 11 13 15 16
  0.000300 10 12 14 15
  0.000200 9 11 12 14
  0.000100 8 9 10 12
  0.000010 4 5 6 7
  e.g., for this sample volume, if the per-voxel-p-value threshold is set at 0.0005, then to keep the probability of getting a single noise-only cluster at 0.05 or less, the cluster size threshold should be 14 voxels.
3. Switch to the directory having the SAM results: e.g., cd /media/sda3/Feng/SAM/erf/
4. Open afni
5. Overlay (fim), underlay (MRI) the related data
6. Move the slide bar until a aimed p-value is reached (e.g., p = 0.0005)
7. Click the Clusterize in the up-right corner of AFNI pad
8. NN level-dafault is 1; Voxels: set the number according to the corrected-value you want to use, for instance, alpha-corrected=0.05, then the number of Voxels should be 14; Click Apply
9. Click Rpt, which is below the Clusterize. You will see a summary of the results which are significant; Press WamI in the Rpt panel, you can get a summary report of the result